## Slide 1: Achieving Montgomery County’s Climate Goals: Sketch of a Vision
2020-10-13
Arjun Makhijani, Ph.D.,
President, Institute for Energy and Environmental Research
www.ieer.org
arjun@ieer.org
December 19, 2013
Annapolis, MD
hijani

## Slide 2: Montgomery County Climate Targets
County is much more ambitious – 80% by 2027; 100% by 2035. Maryland: net zero by 2045 (IEER Plan).
County targets: very tough but could be exemplary for the world, especially local governments.
Buildings are most in the county’s control – almost 50%
Transportation: county and state action needed; state action is crucial.
Will need out-of-the-box ideas to be successful
County compared to IEER state plan
2018 County GHG emissions, total 10.54 million metric tons (NG = natural gas)
Chart: 
Chart: 
| Residential Electricity | Residential fossil fuels (NG) | Commercial Electricity | Commercial fossil fuels (NG) | Transportation fossil fuels (oil) | Rest: HFCs + wastes mainly
 | 1.3196 | 1.2129 | 1.8158 | 0.88972 | 4.3927 | 0.91144

## Slide 3: Today’s Energy System
Generally Reliable - but Lack of Choices
Unaffordable for many
Inflexible, Inefficient. Polluting. Not very resilient
Difficult for democratic control; frequent conflicts over petroleum
Notes: Present system is wasteful, polluting, mostly functioning; not robust or resilient; Maryland sends $10 billion to $12 billion per year out of state to import fuels (oil, natural gas, imported electricity mainly.
https://commons.wikimedia.org/wiki/File:Oil_tanker_Omala_in_Rotterdam.jpg
Photo by Danny Cornelissen

## Slide 4: Thermal electricity generation: Only ~30% of primary energy reaches the home or business
Cattenhom nuclear power plant, France
John Amos coal-fired plant, West Virginia
Notes: John Amos plant: Harry Schaeffer, NARA at https://commons.wikimedia.org/wiki/File:CLOUD_OF_STEAM_RISES_FROM_ONE_OF_THE_MASSIVE_COOLING_TOWERS_OF_THE_JOHN_AMOS_POWER_PLANT_NEAR_NITRO_ON_THE_KANAWHA..._-_NARA_-_551184.jpg; Cattenhom: Seffan Kuhn at https://commons.wikimedia.org/wiki/Nuclear_power_plant#/media/File:Nuclear_Power_Plant_Cattenom.jpg

## Slide 5: Inefficiency: lighting
Incandescent bulb
LED bulb
Incandescent bulb: ~3% of electricity converted to visible light. LED: ~20%.
Notes: Incandescent bulb: De Benutzer KMJ, at https://commons.wikimedia.org/wiki/File:Gluehlampe_01_KMJ.jpg. LED bulb: Dinkar Shukla, at https://commons.wikimedia.org/wiki/File:LED_BULB.jpg

## Slide 6: Inefficiency, example: Automobiles with internal combustion engines; only 1% of energy moves people
Typical gasoline vehicle: 18% to 25% of energy powers the wheels
(not including oil production, pipeline, and refining losses)
Notes: Source: https://www.fueleconomy.gov/feg/atv.shtml

## Slide 7: Inefficiency: Leaky homes, inefficient heating systems
Notes: Source: Home: Icynene Corporation: http://www.insulationsmart.com/stop_major_energy_loss.htm & http://www.insulationsmart.com/images/Major_Air_Leaks_House.gif. For pipeline: Glen Dillon, at https://commons.wikimedia.org/wiki/File:MainLineValve7.jpg.

## Slide 8: Present and Future Grid
Present: One-way communication
Flip switch - turn power on and off.
Future smart grid: Two-way communication.
Consumer has real time information about system.
Appliances are smart and responsive
Consumers can be producers.
Grid operated for reliability and resilience
Adapt to variable energy supply
All of the information in all consumer on-off switches in the United States can be put on one ~$15 USB flash drive
Notes: https://upload.wikimedia.org/wikipedia/commons/a/af/Sandisk_Ultra_USB_Flash_Drive.png Photo by Korail2012

## Slide 9: Grid-of-the-Future Renewable, Resilient, Democratized
Solar and wind mainstays of energy system
Increase efficiency
Storage, combined heat and power, microgrids
Demand response
Control consumption to minimize bills
Electrified transportation and HVAC
Provide services to the grid, including via V2G and local storage ownership
Notes: EPRI's Smart Grid Resource Center. Formerly at http://www.smartgrid.epri.com/. The specific image file was at http://www.smartgrid.epri.com/App_Themes/Default/Images/smart_grid_network_image.gif. Credit: EPRI

## Slide 10: Total primary energy requirements. Requirements include electrification of transportation and buildings. Much lower energy use while economy grows. See Notes 1 and 2
Chart: Total primary energy input, trillion Btu
| 2011 | 2050 BAU | 2050 CPS
Total electricity use | 217.0114 | 284 | 263
Total direct fuel use | 709.68 | 711 | 146
T&D losses | 13.5949 | 18 | 19
Electricity losses (H2 for elec. & DC to AC) | 477.7251 | 557 | 123
Total primary energy input | 1418.0114 | 1570 | 551
Economy ~2x bigger
Primary Energy ~60% lower
Lower Cost than business-as-usual
Notes: Note 1: From Prosperous, Renewable Maryland 2016. Bars not updated to reflect IPCC 2018. Amount of primary energy is calculated as the amount available resulting from the production investment at the first step: the oil or gas wellhead, the coal mine mouth, the solar panel terminals, the wind turbine generator output, etc. For instance, DC to AC conversion losses are taken into account in the case of solar energy.
Note 2: Four major sources of efficiency. i. Elimination of thermal electricity generation. ii, transition from fossil fuel to electric vehicles; iii. Efficient building envelopes, and iv. Efficient electric appliances, including space and water heating with efficient heat pumps and very high efficiency air-conditioners

## Slide 11: Cost Summary, 2016 IEER report: The Year 2050 BAU = Business-as-usual; CPS = Climate Protection Scenario: From Prosperous Renewable Maryland. “High” assumes higher costs and “low” assumes lower costs than the “reference” CPS scenario
Notes: From Prosperous, Renewable Maryland 2016. Not updated to reflect IPCC 2018.
Includes all costs, including smart grid, transportation infrastructure, efficiency, conversion of fossil fuel to efficient electric heating, and the investments needed for the transformation of the electricity system, funds for affordability and Just Transition

## Slide 12: Electricity (~30% of emissions, including building electricity)
IEER Maryland plan: 100% renewable electricity by 2035 or 2040.
The County will need 100% renewable electricity by 2030 at the latest, preferably 2027:
    Community choice energy – power purchase agreements (PPAs) for low-cost wind-generated electricity, ~2,000 MW (no electronic certificates separated from the electricity). There are currently more than 13,000 MW onshore wind projects in the PJM queue with in-service dates before 2030, and mostly before 2027. Ability to do virtual PPAs will be an advantage for the County.
    In-county solar, including individual rooftop and community solar.
    Done well, wind and solar will lower energy costs, provide equity benefits, and give a boost to business.
    Resilience with solar + storage microgrids.
    2 to 3%/year efficiency improvements for existing electricity uses.

## Slide 13: Buildings (~50% of emissions)
Mandate new residential construction to be net-zero-energy starting 2022. Rooftop, net-zero only for detached homes. This is economical and will save consumers money.
Rooftop + dedicated community solar to achieve net-zero-energy for new townhomes, new multi-unit residential buildings, and deep retrofits. These segments need study to create a sound coordinated implementation plan and timetable.
No natural gas connections for new residential buildings starting 2022.
Mandate new commercial construction to be net-zero-energy by 2024. Rooftop, on-site, plus community solar as necessary.
No natural gas connections for new commercial buildings starting 2022.
Convert existing fossil fuel uses in buildings to efficient electric systems by 2035 – needs a detailed plan.

## Slide 14: Transportation (~42% of emissions)
Make public transportation a free public utility, as is being done in some places already. Example: Luxembourg, population 626,000, area 998 sq. miles – about 627 people/square mile. Montgomery County’s population density, a key determinant of feasibility, is more than three times higher.
Ban new petroleum vehicle sales by statewide 2035 (via state law). Work with other counties to get this done and to get Maryland to join California to broaden the adoption of this target. Use the leverage of being the largest and wealthiest county in the state. Focus state rebates for zero emission vehicles on public vehicles (buses, taxis, school buses) and high mileage commercial vehicles (especially small business).
Get state transportation funds to have a wide network safe, exclusive lanes for (non-electric bicycles) and separate exclusive lanes for low power electric bicycles, scooters, etc.
Focus county transportation resources on the above.

## Slide 15: Annapolis to-do list (in addition to transportation items)
Form a County Annapolis team focused to get state policies the county needs for its climate goals
Get Community Choice Energy legislation passed for the County.
Double the solar net metering to 3,000 megawatts.
Enable smart grid infrastructure regulatory rules and utility business models
Increase EmPOWER efficiency goal to 3% per year.
Enact an affordable energy program: limit residential energy bills of eligible low-income households to 6% of gross income.
Ban new fossil fuel-related investments like natural gas pipelines to minimize stranded asset risk.
Establish the Maryland Center for Agricultural and Industrial Sustainability so as to reduce emissions impact of materials to zero and then turn it negative at the latest by the 2040s.

## Slide 16: “Out-of-the-box” ideas
The County’s climate targets, (80% GHG reduction by 2027, 100% by 2035) are “out-of-the-box.” It needs ideas to match. For example:
Give property tax rebates for converting residential lawns to organic food production; support them with suitable marketing, infrastructure, and policies.
Tax residential lawns above 10,000 square feet per house.
Turn buildings into carbon sequestration centers – hempcrete, for instance.
Join energy, transportation, residential, commercial, agricultural land use planning throughout the county to encourage easy, safe access to healthy local food, local commerce, and to improve soil health, sequester carbon, and stimulate the local economy – all while reducing greenhouse gas emissions.

## Slide 17: Where will the money come from? Wealth tax: 1 percent of the 0.1 percent
Tax the wealth of the top 0.1 percent of state households (about 2,200 households) at 1 percent per year. This should be a principal objective in Annapolis.
Estimated state revenue, based on national data, roughly $3 billion per year. County share, based on population, about $500 million. The state’s COVID-19 related deficit is on the order of $1 billion.
A wealth tax won’t reduce the wealth of the wealthy, just slow down its growth because assets of the wealthy typically grow at far more than 1% per year.
Example: Bill Gates had $63 billon in 2000 when created a foundation. He has given billions to the foundation, whose assets grew to $51 billion. His total giving since 1994 was reportedly ~$45 billion. His wealth in 2020: $115 billion.

## Slide 18: Resources
Renewable Maryland Project webpage with links to many publications
Prosperous, Renewable Maryland
Beyond a Band-Aid – Just transition paper – with Labor Network for Sustainability
Energy justice in Maryland – equity and affordability book and infographic
IEER 2015 report on conversion of buildings from fossil fuels to efficient electric systems
IPCC 2018 Summary for Policymakers and URL from which other chapters can be downloaded